## Slide 1: Detection of live radionuclides in stony meteorites by accelerator mass spectrometry – with and without tedious chemical sample preparation Martin Martschini, Oscar Marchhart, Silke Merchel, Alexander Wieser, Robin Golser & more people University of Vienna, Faculty of Physics, Isotope Physics, VERA Laboratory, Austria silke.merchel@univie.ac.at

## Slide 2: Detection of live radionuclides in stony meteorites by accelerator mass spectrometry – with and without tedious chemical sample preparation Martin Martschini, Oscar Marchhart, Silke Merchel, Alexander Wieser, Robin Golser & more people University of Vienna, Faculty of Physics, Isotope Physics, VERA Laboratory, Austria silke.merchel@univie.ac.at
Introduction
  (Stony) meteorites
  Cosmogenic nuclides (CNs)
  Example with chemistry
Accelerator mass spectrometry (AMS) @ VERA
Examples without chemistry

## Slide 3
Earth’s atmosphere & magnetic field
meteorite (terrestrial age)
meteoroid parent body (possible pre-exposure in regolith)
meteoroid
impact
cosmic rays
cosmic ray
exposure (CRE)
Unknowns:
tirr. @ MPB
depth @ MPB
rpreatm.
tirr.
depth
tterr. (find)
Cosmogenic nuclides in meteorites

## Slide 4
Unknowns:
tirr. @ MPB
depth @ MPB
rpreatm.
tirr.
depth
tterr. (find)
Cosmogenic nuclides in meteorites
Solution:
Multi-nuclides (stable & radioactive)
MC with individual chemistry

## Slide 5
Ksar Ghilane 002, the 100th Martian meteorite
J. Llorca et al., MAPS, 2013.
13th Jan 2010
Tunisia
538 g
paired with Los Angeles? (Mojave Desert 1999)
10 x 4.5 x 3.5 cm3
1.5 cm
~ 200 mg
Notes: Pulver 3 cm Bildlaenge
Name: Ksar Ghilane 002 This is an OFFICIAL meteorite name. Abbreviation: KG 002 Observed fall: No Year found: 13. January 2010 Country: Tunisia Mass: 538 g

## Slide 6
Ksar Ghilane 002 10Be & 26Al
1.5 cm
rpreatm. = 35-65 cm centre position
tirr. = 2.8-3.7 Ma
Los Angeles: rpreatm. = 20-40 cm tirr. = 2.8-3.3 Ma
J. Llorca et al., MAPS, 2013.
similar element composition, petrography & mineral chemistry, plus noble gases
suggesting a possible launch-pairing
~ 200 mg
Notes: Pulver 3 cm Bildlaenge
Name: Ksar Ghilane 002 This is an OFFICIAL meteorite name. Abbreviation: KG 002 Observed fall: No Year found: 1. January 2010 Country: Tunisia Mass: 538 g
undersaturated (10Be)
highest 26Al ever: (116.1 ± 1.9) dpm/kg GCR only (27Al)

## Slide 7
Earth’s atmosphere & magnetic field
meteorite (terrestrial age)
meteoroid parent body (possible pre-exposure in regolith)
meteoroid
impact
cosmic rays
cosmic ray
exposure (CRE)
Meteorite’s history

## Slide 8
Earth’s atmosphere & magnetic field
meteorite (terrestrial age)
meteoroid parent body (possible pre-exposure in regolith)
meteoroid
impact
cosmic rays
cosmic ray
exposure (CRE)
chemistry
AMS
e.g. BeO
e.g. 10Be
Meteorite’s history

## Slide 9
Extracting live cosmogenic nuclides from meteorites
Merchel & Herpers, RCA (1999).
~ 100 mg
dissolution (HF)
evaporation
ion exchange
precipitation
Notes: No Zr-93 and Fe-60 @ Munich anymore…

## Slide 10
Extracting live cosmogenic nuclides from meteorites
Merchel & Herpers, RCA (1999).
dissolution (HF)
evaporation
ion exchange
precipitation
~ 100 mg
www.zvab.com/servlet/BookDetailsPL?bi=30730238164&searchurl=sortby%3D20%26tn%3Dansichtskarte%2Baschenputtel%2Btauben&cm_sp=snippet-_-srp1-_-image4#&gid=1&pid=1
Notes: No Zr-93 and Fe-60 @ Munich anymore…

## Slide 11
Merchel & Herpers, RCA (1999).
dissolution (HF)
evaporation
ion exchange
precipitation
~ 100 mg
Extracting live cosmogenic nuclides from meteorites
Notes: No Zr-93 and Fe-60 @ Munich anymore…

## Slide 12: Detection of live radionuclides in stony meteorites by accelerator mass spectrometry – with and without tedious chemical sample preparation Martin Martschini, Oscar Marchhart, Silke Merchel, Alexander Wieser, Robin Golser & more people University of Vienna, Faculty of Physics, Isotope Physics, VERA Laboratory, Austria silke.merchel@univie.ac.at
Introduction
  (Stony) meteorites
  Cosmogenic nuclides (CNs)
  Example with chemistry
Accelerator mass spectrometry (AMS) @ VERA
Examples without chemistry

## Slide 13
Radionuclides @ VERA
Ion Laser Interaction Mass Spectrometry
t1/2: ~1 a – 80 Ma
Notes: No Zr-93 and Fe-60 @ Munich anymore…

## Slide 14
Cosmogenic nuclides @ VERA
Ion Laser Interaction Mass Spectrometry
t1/2: 0.6 – 4 Ma
Notes: No Zr-93 and Fe-60 @ Munich anymore…

## Slide 15
VERA – 3 MV Tandem

## Slide 16
VERA – 3 MV Tandem

## Slide 17
VERA & ILIAMS (26Al – t1/2=0.7 Ma)

## Slide 18
VERA & ILIAMS (26Al)
Ion- Laser Inter Action Mass Spectrometry
HE (MeV) MS (+)
LE (keV) MS (-)
[last talk tomorrow by Alex!]
stripping  no molecules
 “no”
isobars

## Slide 19
VERA & ILIAMS (26Al)
40-sample Cs sputter source
Al2O3/Fe in Cu/Cu
AlO-
30 kV pre- acceleration
90° bending magnet
laser set-up
RFQ ion cooler
Al3+
injection magnet
analyzing magnet
tandem @2.95 MV
Ar stripper
27AlO-
27Al3+
MgO-
Off-Set FC
Off-Set FC
2-anode gas ionization chamber
26Al3+

## Slide 20
ILIAMS for 26Al
AlO-, Cl-, CsF2-, SrF3-, TcF5-
Cs-, FeH-
TcF5-
CaF3-
532 nm
Martschini et al., Radiocarbon 2021. Lachner et al., Int. J. Mass Spectr. 2021.
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 21
ILIAMS for 26Al
AlO-, Cl-, CsF2-, SrF3-, TcF5-
Cs-, FeH-
TcF5-
CaF3-
532 nm
   Isobar suppression (26Mg) ~1011
Martschini et al., Radiocarbon 2021. Lachner et al., Int. J. Mass Spectr. 2021.
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 22
ILIAMS for 26Al (AlO-)
Al-  AlO-  10 x current 
2.95 MV & 3+ (unchanged)
28% stripper yield (Ar)
54% cooler
+ ionis. eff. (~1.5%)
+ detector eff. (100%)
   0.23% total efficiency
   3  5 x more counts / time / sample
Martschini et al., Radiocarbon 2021. Lachner et al., Int. J. Mass Spectr. 2021.
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 23
ILIAMS for 26Al (AlO-)
Martschini et al., Radiocarbon 2021. Lachner et al., Int. J. Mass Spectr. 2021.
Al-  AlO-  10 x current 
2.95 MV & 3+ (unchanged)
28% stripper yield (Ar)
54% cooler
+ ionis. eff. (~1.5%)
+ detector eff. (100%)
   0.23% total efficiency
   3  5 x more counts / time / sample
   Background 26Al / 27Al = 5 x 10-16
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 24
ILIAMS for 26Al (AlO-)
Al-  AlO-  10 x current 
2.95 MV & 3+ (unchanged)
28% stripper yield (Ar)
54% cooler
+ ionis. eff. (~1.5%)
+ detector eff. (100%)
   0.23% total efficiency
   3  5 x more counts / time / sample
   Background 26Al / 27Al = 5 x 10-16
   Isobar suppression (26Mg) ~1011
Martschini et al., Radiocarbon 2021. Lachner et al., Int. J. Mass Spectr. 2021.
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 25: Detection of live radionuclides in stony meteorites by accelerator mass spectrometry – with and without tedious chemical sample preparation Martin Martschini, Oscar Marchhart, Silke Merchel, Alexander Wieser, Robin Golser & more people University of Vienna, Faculty of Physics, Isotope Physics, VERA Laboratory, Austria silke.merchel@univie.ac.at
Introduction
  (Stony) meteorites
  Cosmogenic nuclides (CNs)
  Example with chemistry
Accelerator mass spectrometry (AMS) @ VERA
Examples without chemistry

## Slide 26
Extracting live cosmogenic nuclides from meteorites
Merchel & Herpers, RCA (1999).
dissolution (HF)
evaporation
ion exchange
precipitation
~ 100 mg
Notes: No Zr-93 and Fe-60 @ Munich anymore…

## Slide 27
26Al – No chemistry !
*https://fundus.uni-hamburg.de/de/ collection_records/26856#pfad U. Neupert, diploma thesis,U Hanover (1993). S. Merchel, PhD thesis, U Cologne (1998).
LL6 chondrite Dhurmsala (32 kg, Fall, India, 1860)
1.2% Al
14.9% Mg (1.6% 26Mg)
   22 nA AlO- (chem.  µA)  100 counts min-1 sputtering  3 mg lasts > 5 h  3% uncert. in 15 min
*
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 28
26Al – No chemistry !
*https://fundus.uni-hamburg.de/de/ collection_records/26856#pfad U. Neupert, diploma thesis,U Hanover (1993). S. Merchel, PhD thesis, U Cologne (1998).
LL6 chondrite Dhurmsala
*
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 29
26Al – No chemistry !
*https://fundus.uni-hamburg.de/de/ collection_records/26856#pfad U. Neupert, diploma thesis,U Hanover (1993). S. Merchel, PhD thesis, U Cologne (1998).
LL6 chondrite Dhurmsala
*
  we need low-current standard for better accuracy!
  Dhurmsala!
Notes: Talk of Markus Schiffer
https://www2.chemistry.msu.edu/faculty/reusch/virttxtjml/spectrpy/uv-vis/spectrum.htm

## Slide 30
26Al in fake meteorites
24 mm
“Baraka Landi”
800 g found (gold prospector) South Libya, 15th Feb 2021
26Al/27Al <1.1∙10-13
 0.06 dpm/kg (no 27Al data) (~1000 x < Dhurmsala)
Libya
Chad
Niger
© Dieter Heinlein
800 g

## Slide 31
26Al in fake meteorites
Not “Thurnau”
piece recently found in strewn field of fireball, Oberfranken, Germany (4th Feb 2016)
“dark matrix”
26Al/27Al <7∙10-13
 <2 dpm/kg (7.5% (!!!) 27Al)*
Strewn field of the Thurnau meteorite fall (based on wind profiles of the weather stations Kümmersbruck (blue) and Meiningen (yellow) ,plus mean (red) for fragments between 10 g and 1 kg. Expected main mass 300 g (data & figure by Pavel Spurný).
*priv.com. Dieter Heinlein (2021).

## Slide 32
26Al in fake meteorites
“FRH-1-2-2-C”
6 kg piece recently found in Southern Germany
26Al/27Al <2.4∙10-13
 <0.13 dpm/kg (no 27Al data)
© Dieter Heinlein
1 cm
Notes: All good things come in threes

## Slide 33
26Al in meteorites
©
https://www.lpi.usra.edu/meteor/get_original_photo.php?recno=5677833
https://www.youtube.com/watch?v=Qj94c_YRNU0
*Marrocchi et al., ApJL 913 (2021) L9.
Tarda
C2 (ungrouped) carbonaceous chondrite
fall, Moroccan Sahara, 25th Aug 2020 strewn field, ∑ = 4 kg
~3000 26Al counts  26Al/27Al = (7.7 ± 0.5)∙10-11
 (35.5 ± 2.3) dpm/kg (1.1% 27Al)*

## Slide 34
26Al in meteorites
©
https://www.lpi.usra.edu/meteor/get_original_photo.php?recno=5677833
https://www.youtube.com/watch?v=Qj94c_YRNU0
*Marrocchi et al., ApJL 913 (2021) L9.
Tarda
C2 (ungrouped) carbonaceous chondrite
fall, Moroccan Sahara, 25th Aug 2020 strewn field, ∑ = 4 kg
~3000 26Al counts  26Al/27Al = (7.7 ± 0.5)∙10-11
 (35.5 ± 2.3) dpm/kg (1.1% 27Al)*

## Slide 35
26Al in meteorites
©
https://www.nhm-wien.ac.at/ludovic_ferriere
https://www.lpi.usra.edu/meteor/metbull.php?code=75426
https://de.wikipedia.org/wiki/Kindberg_(Meteorit)
Kindberg
L6 ordinary chondrite
1st Austrian meteorites after 44 years
fall, Styria, Austria, 19th Nov 2020
single piece: 233 g (4th July 2021)
>9000 26Al counts 26Al/27Al = (1.33 ± 0.08)∙10-10
 ??? dpm/kg (no 27Al data yet)

## Slide 36
*https://fundus.uni-hamburg.de/de/ collection_records/26856#pfad Martschini et al., Radiocarbon (2021).
Dhurmsala
~1‰ K (~60 µg/g 41K)
mixed with PbF2 (1:9)  CaF3-
   1 41Ca count min-1
*
   Isobar suppression (41K) ~1011
41Ca (t1/2=0.1 Ma) in meteorites

## Slide 37
41Ca (t1/2=0.1 Ma) in meteorites
*https://fundus.uni-hamburg.de/de/ collection_records/26856#pfad Martschini et al., Radiocarbon (2021).
Dhurmsala
~1‰ K (~60 µg/g 41K)
mixed with PbF2 (1:9)  CaF3-
     1 41Ca count min-1
*
   Isobar suppression (41K) ~1011

## Slide 38
Other “interesting” stuff ?
10Be, 26Al, 36Cl, 41Ca data traceable to primary AMS standards*
(help in) improving “routine” chemistry: ice, in-situ, sediments, deep-sea MnFe…
further information see...
*Merchel & Bremser 2004; Merchel et al. 2011, 2012, 2019a/b; Arnold et al. 2010, 2013; Akhmadaliev et al. 2013; Rugel et al. 2016 ,…
ChETEC-INFRA tour given by M. Martschini now @ https://isotopenphysik.univie.ac.at/oeffentlichkeitsarbeit/
  We are grateful to Ludovic Ferrière, Dieter Heinlein & Erik Strub for providing (precious) samples.
Conclusion:
I am getting rid of my chemist’s job (for meteorites)!

## Slide 40
“Stacked-foil absorber” (10Be)
Schmidt, Master thesis, U Vienna (2013).
(now: 16 mm)
5 mm x 5 mm (~13)*  10 mm x 10 mm Si3N4 (~8)  = 7 µm  detector eff. (~85%)
3+  2+  5%  55% stripper (Ar) yield
*Steier et al., Int. J. Mass Spectr. 444 (2019).
Notes: 13 foils; ~ 7 µm, , 5 x 5 mm2 (Steier et al., 2019), Silson
2+ stripper yield
after 2 h: 75% of BeO are used after 1 h: 1/3 of BeO used

## Slide 41
“Stacked-foil absorber” (10Be)
*Steier et al., Int. J. Mass Spectr. 444 (2019).
5 mm x 5 mm (~13)*  10 mm x 10 mm Si3N4 (~8)  = 7 µm  detector eff. (~85%)
3+  2+  5%  55% stripper (Ar) yield
+ ionis. eff. (~2%)
   1% total eff. 
Notes: 13 foils; ~ 7 µm, , 5 x 5 mm2 (Steier et al., 2019), Silson
2+ stripper yield
after 2 h: 75% of BeO are used after 1 h: 1/3 of BeO used

## Slide 42
ILIAMS